## Slide 1
Smart Irrigation System
IoT-Based Automated Water Management
Course: Design Engineering Project (DEP) | CP301
Department:
Electrical Engineering & Computer Science, IIT Ropar
Rahul (2023 EEB 1238) Kunal Dhiman (2023EEB1218)
Supervisors: Prof. Jagpreet Singh (CSE) & Prof. Saifullah Payami (EE)
IIT Ropar

## Slide 2
Problem Statement
Water Wastage
Traditional irrigation wastes 50-70% of water due to over-watering and lack of feedback systems.
Manual Operation
Farmers must manually monitor and control irrigation, which is time-consuming and error-prone.
No Real-Time Data
Absence of real-time soil moisture data prevents timely irrigation decisions, impacting crop yield.
Remote Fields
Fields are often far from the operator, making manual checks impractical and costly.

## Slide 3
System Overview
ESP32
(Field Side)
Moisture Sensor
▶
AWS Cloud
(MQTT Broker)
IoT Core + Rules
▶
ESP32
(Motor Side)
Valve Controller
Mobile App
Real-time monitoring
& control interface

## Slide 4
Technical Architecture
⚙️ Hardware Stack
2× ESP32 Microcontrollers (Wi-Fi enabled)
Capacitive Soil Moisture Sensor
Water Pump / Solenoid Valve
Motor Driver Module (L298N)
Custom PCB & enclosure housing
Power supply via 5V adapter
☁️ Software Stack
AWS IoT Core — MQTT message broker
MQTT Protocol for pub/sub messaging
AWS Lambda — trigger-based automation
Amazon DynamoDB — data logging
Mobile App (Flutter/Android)
Arduino IDE — ESP32 firmware

## Slide 5
How It Works
1
Sense
Soil moisture sensor (ESP32 #1) continuously reads moisture level in the field.
2
Threshold Check
If moisture drops below 73%, the ESP32 triggers an alert message.
3
Publish to Cloud
Alert is published via MQTT to AWS IoT Core topic from the field ESP32.
4
Subscribe & Act
Motor-side ESP32 subscribes to the topic, receives message, opens valve.
5
Irrigate
Water valve opens; field is irrigated. Sensor value is monitored continuously.
6
App Monitoring
Mobile app shows live soil moisture % and motor ON/OFF status in real time.

## Slide 6
Communication: From ESP-NOW to AWS MQTT
Phase 1 — ESP-NOW (Deprecated)
Peer-to-peer Wi-Fi protocol
Very fast & low latency
❌ Range limited to ~200m
❌ No internet/cloud connectivity
❌ Both ESP32s must be in proximity
❌ Not scalable or remotely operable
→
Phase 2 — AWS MQTT (Current)
Cloud-based pub/sub messaging
✅ Unlimited range via internet
✅ Real-time global communication
✅ AWS IoT Core reliability & security
✅ Supports data logging & analytics
✅ App integration & remote control
⚡ Key Insight: Switching to cloud-based MQTT removed range constraints and enabled a fully scalable, internet-connected solution.

## Slide 7
Mobile Application
Live Soil Moisture
Displays current soil moisture percentage in real-time, updated continuously from sensor readings via MQTT.
Motor Status
Shows whether the irrigation motor/valve is currently ON or OFF with visual indicator.
Wireless Updates
Data pushed instantly from ESP32 through AWS cloud to the app — no manual refresh needed.
Historical Logs
View past moisture readings and irrigation events stored in AWS DynamoDB for analysis.
"A complete end-to-end system — from soil to smartphone"

## Slide 8
Results & Demonstration
73%
Moisture Threshold
Precisely calibrated trigger point
<2s
Response Time
Sensor to valve actuation
∞
Operating Range
With AWS cloud (internet-based)
24/7
Auto Monitoring
No manual intervention needed
✅ Project Deliverables Achieved
Fully working physical prototype with two ESP32 boards
Real-time moisture monitoring and automated valve control
Cloud integration via AWS IoT Core with MQTT protocol
Functional mobile app with live dashboard
End-to-end tested with measurable response time under 2 seconds

## Slide 9
Future Scope & Upgrades
Solar Power Integration
Equip the field-side ESP32 unit with solar panels for off-grid, self-sustainable operation — ideal for remote agricultural areas.
AI-Based Predictive Irrigation
Integrate weather forecast APIs and ML models to predict irrigation needs proactively based on weather patterns and crop type.
LoRa / NB-IoT for Deep Rural Areas
Replace Wi-Fi with LoRa or NB-IoT in areas without internet, extending system viability to the most remote farmlands.
Enhanced App with Analytics
Add historical trend charts, crop-specific moisture profiles, daily/weekly usage reports, and alert notifications.
Multi-Zone Irrigation
Scale system to manage multiple irrigation zones independently — each zone with its own sensor and valve pair.
OTA Firmware Updates
Enable over-the-air updates for both ESP32 nodes so the system can be upgraded without physical access to hardware.

## Slide 10
Conclusion
Designed and built a fully functional smart irrigation prototype using ESP32, AWS IoT Core, and MQTT.
Successfully automated valve control based on real-time soil moisture thresholds — reducing human intervention.
Evolved communication from ESP-NOW (limited range) to cloud-based MQTT for unlimited remote operation.
Developed a live mobile app dashboard for monitoring and control from anywhere.
Laid a strong foundation for AI-driven, solar-powered, and multi-zone smart farming solutions.
Rahul (2023EEB1238) · Kunal Dhiman (2023EEB1218) · IIT Ropar — CP301
Thank You!